## Slide 1: Introduction to Eclipse, RobotBuilder and FRCSIM
Dave Frederick, Mentor
Team 1895, Manassas, VA
December 3, 2016 Version 1.0

## Slide 2: Goal of Workshop
Demonstrate a process to create a basic Robot using Eclipse and RobotBuilder
Demonstrate the FRCSIM (Robot Simulator)
WPI (Worcester Polytechnic Institute) Robot Builder Resource:
https://wpilib.screenstepslive.com/s/4485/m/26402

## Slide 3: Process to Build Robot Software - Overview
Design the Robot on Paper
Build Robot in RobotBuilder
  Create subsystems, commands and Operator Interface
Import RobotBuilder into Eclipse
Finish the Software in Eclipse
  Create methods within the subsystems to implement commands
Deploy, Test, Troubleshoot
Expand, Revise, Enhance

## Slide 4: Step 1: Design the Robot
Understand the Game then Design the Robot
Define the Requirements for the Robot
  Understand how to play the Game and scoring
  Decide how your Team will play the game
  Decide what your robot needs to do
Create an initial design of the Robot and decompose into Subsystems
  Identify Subsystems: Drive Train, Shooter/Manipulator
  Design the User Interface: Joystick control functions, Smart Dashboard
  Identify what the robot will do: autonomous actions, drive behavior, arm movements
Software High Level Design
  Determine what functions/actions the subsystems must do. Document requirements
  Determine the best approach for the User Interface, How do you drive the robot?

## Slide 6: Software Design
Think about the sensors to include in the subsystems
Drivetrain should include the sensors to measure distance, heading and range to target
This allows high level commands to be given to the subsystem
For example, Move forward 2 feet, turn 90 degrees
Object Oriented Design:
Details of the Object implementation are kept within the subsystem

## Slide 7: Software Design – Subsystem Requirements
DriveTrain:
Requirements:
  Move forward, backward, and rotate
  Maximum forward speed: 2 feet/Second (Fast)
  Drive in a straight line in autonomous mode
  Can turn 90 degrees on command
  Can move forward 4 feet on command
  Drive with single joystick
Implementation:
  Tank Drive : 4 Motors
  Sensors: Shaft Encoders and a Gyro

## Slide 8: Software Design
Document each subsystem methods and commands
Subsystems
  Drive Train – 4 motor
    Commands:
      Stop, manual drive with joystick
      Drive forward until 5 feet from wall
      Turn Right 90 degrees, Turn Left 90 degrees
      Move forward x feet
  Arm/Manipulator
    Commands:
      Stop, manual drive with left and right buttons
      Move to setpoint
  Operator Interface
    Single Joystick: X and Y axis
    3 Buttons: Move arm left, Move arm to Center, Move arm to right

## Slide 9: Step 2: Build Robot in RobotBuilder Start and Initialize RobotBuilder Project
Eclipse => WIPLib => Run RobotBuilder
On Creation of new Robot Project, set:
  Project Name: e.g.: RobotOne
  Team Number: e.g.: 1895
In Robot Project, set:
  Java Package: e.g.: “Team1895.RobotOne”
  Eclipse Workspace: e.g.: “C:\_Robotics\2016\Eclipse_Projects”
    See current workspace: Eclipse => File => Switch Workspace => Other
  Wiring File: e.g.: “C:\_Robotics\2016\Eclipse_Projects\RobotOneWires”
Save the RobotBuilder Project file
  Select RobotBuilder => Save As => “C:\_Robotics\2016\Eclipse_Projects\RobotOne”
A package is a namespace that organizes a set of related classes and interfaces. Conceptually you can think of packages as being similar to different folders on your computer.

## Slide 10
Robot Builder – First startup

## Slide 11: Build Robot in RobotBuilder
Create
  Subsystems
  Commands for subsystems
  Operator Interface
    Add a JoyStick
    Add a Button on the JoyStick
  Associate Buttons with Commands

## Slide 12
Add subsystems, Joysticks, and sensors by right clicking and selecting

## Slide 15
Robot Builder – Explorer and Wiring Diagram

## Slide 16: Step 3: Import RobotBuilder into Eclipse
Save the RobotBuilder Project
  Select RobotBuilder => Save As => “C:\_Robotics\2016\Eclipse_Projects\RobotOne”
Export the Java Code
  Select RobotBuilder => Export => Java Or “Java” on the Menu
Import the Java Project into Eclipse
  Select Eclipse => File => Import => General => Existing Projects into Workspace
  Browse to project folder: e.g.: “C:\_Robotics\2016\Eclipse_Projects\RobotOne”

## Slide 17
RobotBuilder Project
Resulting JAVA Project in Eclipse
Robot Overhead

## Slide 19: Step 4: Finish the Software in Eclipse Detailed Coding Begins ……….
At this point you have a lot of code that does nothing!
Need to tie inputs to outputs using methods
Need to create Methods() within the Subsystems
Commands call Methods ()
User Interface calls Commands
A “Command” object Tells a “Subsystem” object to do something by way of “Methods”

## Slide 20: Enter the FRC IterativeRobot Class
RobotBuilder creates an framework or template based on the IterativeRobot
Supports:
Robot software initialization
Autonomous mode
TeleOperate mode
During development, the operating mode is selected by the DriversStation
During Competition, the mode is controlled by the Field Management System

## Slide 21: High level structure of the IterativeRobot
Power On
Runs robotInit() method
Initializes all of the defined subsystems (Runs constructors)
Runs OI() method
  Initializes the Operator Interface (Runs constructors)
Runs disabledInit() method once
Runs disabledPeriodic() method REPEATEDLY
Runs autonomousInit() method once
autonomousPeriodic() method REPEATEDLY
teleopInit() method once
teleopPeriodic() method REPEATEDLY
15 Seconds
2 Minutes
Waiting for Go

## Slide 22
Checks for Operator Interface actions
Links the commands to be run
Calls the methods in the subsystem and runs one time
  Gets input
  Processes
  Sets output
teleopPeriodic() method
Code run in continuous loop for autonomousPeriodic() or teleopPeriodic()
Loop is call 50 times per second (Wow!)

## Slide 23: Simple Example of a Control Flow
JoyStick button initiates a command
Command calls a subsystem method
Subsystem method signals a motor controller
Motor controller makes the wheels turn or an arm move!

## Slide 24
Simple Example – Operator Interface Calls the Command
When Button 2 is pushed, the command to Move the Arm is run

## Slide 25
Commands call Subsystem Methods
Simple Example – Commands Calls the Subsystem Method

## Slide 26
Methods Control the hardware with primitive commands
.Set(0.5) [Mid point]
.set(1.0)
[Full clockwise]
.Set(0.0)
[Full Counter
Clockwise]
Simple Example –Subsystem Method controls Hardware

## Slide 27: Commands
The Command based approach provides a great deal of flexibility
When a command is called you can call methods:
Call a subsystem method one time at the beginning
Repeatedly
Call a subsystem method one time at the end of a command

## Slide 28: Options for Commands
public class Arm_MovetoCenter extends Command {
// Class Constructor
public Arm_MovetoCenter() {
requires(Robot.arm);
}
// Called just before this Command runs the first time
protected void initialize() {
}
// Called repeatedly (50 times per second) when this Command is scheduled to run
protected void execute() {
}
// Make this return true when this Command no longer needs to run execute()
protected boolean isFinished() {
return false;
}
// Called once after isFinished returns true
protected void end() {
}
// Called when another command which requires one or more of the same
// subsystems is scheduled to run
protected void interrupted() {
}
}

## Slide 29: Default Command
The command performed when no other commands are given to a subsystem
Each subsystem may, but is not required to, have a default command which is scheduled whenever the subsystem is idle
The most common example of a default command is a command for the drivetrain that implements the normal joystick control.

## Slide 30: Default Command

## Slide 31: Autonomous Command
Create an Autonomous Command Group
Tells the Robot what to do when in Autonomous Mode
Consists of a sequence of other command
Performed in series or parallel
Start of Autonomous
Move Forward
4 feet
Turn Right 90 degrees
Raise Arm
Move to exactly 6 feet from Target
Shoot Ball
Notice how these actions are performed in parallel

## Slide 32: Go!
Compile => Deploy => Execute

## Slide 33: Compile and Deploy

## Slide 34: Console Display of Successful Deployment

## Slide 35
Smart Dashboard

## Slide 36: Start the Smart Dashboard

## Slide 37: Initial Checkout!
Lift Robot wheels off of ground to prevent sudden unplanned movement
Keep hands, fingers and hair away from Robot
Test one function at a time
Observe and think
Take Notes
Think Safety!
Our Robots may not follow "Asimov's Three Laws of Robotics"
“1) A robot may not injure a human being …”

## Slide 38: Updating the Code to Solve Problems
Code update can be performed either in Eclipse or RobotBuilder
In Eclipse, edit code directly. Always add comments
In RobotBuilder:
Re-Open RobotBuilder, Make the required updates, then export
In Eclipse, Refresh the project by selecting “F5”
The robotBuilder updates will be shown, User provided code remains
Don’t edit code between the RobotBuilder comments

## Slide 39: Step 5: Test, Troubleshoot, Resolve Iterative Process…
Test
Troubleshoot
Resolve

## Slide 40: Troubleshooting Methods:
1) Print statements to the System Console (Riolog)
System.out.println("Ball Release Going Out");
Smart Dashboard
Many other approaches …
Console

## Slide 41: FRCSIM (a WPI Implementation of Gazebo Robot Simulator)
FRCSIM provides a means to develop software and run in a Simulator
High Level Process:
Create Robot in SolidWorks
Enhance with motors and sensors with the FRC SolidWorks Gazebo Plugin
Export Robot and World
Open robot and world Gazebo
Develop and Run code in Eclipse

## Slide 42: 1) Create Robot in SolidWorks

## Slide 43: 2) Enhance with motors and sensors with SolidWork’s Gazebo Plugin

## Slide 44: 4) Open the Robot Model in Gazebo

## Slide 45: 5) Develop and Run code in Eclipse

## Slide 46: 6) Running the Simulation

## Slide 47
Questions?

## Slide 48
Manassas, VA
Osbourn High school

## Slide 49
My career: BS - Electrical Engineering (Univ. of South Carolina, 1983)
  Commercial Satellite Communications
  Military Communications (Robust HF Radios)
  Military Communications Maintenance Training Simulators
  Military Flight Simulators (Helicopters)
  Military Communications on Helicopters
  Military Electronic Communication Systems (Secure Email)
Roles:
  System Engineering – Figuring out what needs to be made
  Integration and Test - Making new systems work the first time
  Information Assurance – Protecting our systems

## Slide 50: Resources
Guidance
https://wpilib.screenstepslive.com/s/4485
WPI Library
http://first.wpi.edu/FRC/roborio/stable/docs/java
http://first.wpi.edu/FRC/roborio/stable/docs/java/classedu_1_1wpi_1_1first_1_1wpilibj_1_1command_1_1WaitCommand.html
Eclipse:
http://help.eclipse.org/luna/index.jsp?topic=%2Forg.eclipse.cdt.doc.user%2Ftasks%2Fcdt_t_comment_out.htm
FRC Roborio eclipse plugins zip file
http://first.wpi.edu/FRC/roborio/zipfile/
WPI ThinkTank
http://thinktank.wpi.edu/Portal
FRCSIM Resources:
https://wpilib.screenstepslive.com/s/4485/m/23353
http://first.wpi.edu/FRC/roborio/release/simulation/